KEITH COUNTY FAIR 2019

COMBINE DEMOLITION DERBY

RULES AND REGULATIONS

FRIDAY JULY 26th at 6:00

# ENTRY PREPARATION

- ALL GLASS MUST BE REMOVED FROM CAB INCLULDING LIGHTS.

- ANY SHARP OR PROTRUDING ITEMS NEED TO BE FLATTENED OR REMOVED.

- RADIATORS, TRANSMISSION COOLERS MUST REMAIN IN ORIGINAL LOCATION OR BE REMOVED.

- FAN SHROUDS MAY BE REMOVED.

- ELECTRONICS MAY BE ALTERED.

- FUEL CELL MUST BE PLACED INSIDE THE GRAIN TANK WITH NO SPILL TYPE CAP.

- COMBINE MUST HAVE A REINFORCED CAB WITH DOOR CHAINED OR WELDED OR BE EQUIPPED WITH ADEQUATE ROLL-OVER PROTECTION.  A SATISFACTORY HORIZONTAL BAR MUST BE WELDED ON THE DRIVERS CAGE FOR ADDED PROTECTION AND MUST PASS INSPECTION BY DERBY OFFICIAL.

- BATTERIES MUST BE SECURED IN A SAFE AREA SUCH AS GRAIN TANK OR ENGINE COMPARTMENT.

- GRAIN TABLE ONLY, NO CORN HEADS, CUTTING SYSTEM AND REEL TO BE REMOVED.

- BRACING CAN BE ADDED FROM THE COMBINE FEEDER HOUSE TO EDGE OF PLATFORM NOT TO EXCEED THE ORIGINAL WIDTH OF THE PLATFORM.  WELDING WHOLE MACHINE IS UNLIMIED ONLY 8 PIECES OF IRON CAN BE ADDED TO FEEDER HOUSE AND HEAD ONLY 6” X 6” PLATES.

- GRAIN TABLE MUST BE PERMANENTLY LOCKED OR LIFT CYLINDERS REMOVED AT A HEIGHT OF 18” TO 22” AT CUTTER BAR.

- RUBBER TIRES WITH AIR ONLY, NO OTHER FLUIDS OR FOAM, NO DUALS, AND ETC.

- DISCHARGE AUGERS, CAB LADDER, SEPARATOR DRIVE BELT AND STRAW CHOPPERS MUST BE REMOVED.

- PROTECTION MAY BE PUT ON STEERING CYLINDER ONLY AS BIG AS CYLINDER ASSY.